## Slide 1: Thesis Update #11
June 3, 2019
James Erik Groving Meade

## Slide 2: Hardware Model Update Overview
Implemented and verified backpropagation architecture for all layers
Implemented and verified weight update phase
Implemented a state machine for each layer to allow “looping” through the states, i.e:
  Forward – wait for gradients to be ready – backward – update weights – forward – ….

## Slide 3: Verification of BP for FC0 and FC1 layers
There are 76,832 gradients for FC0 and 6,664 for FC1… I’ll just randomly choose a few gradients for this ppt

## Slide 4: Layer States Currently designed to train constantly over provided input

## Slide 5: Update Architecture
Idea – Iterate a pointer over the BRAM, updating weights as you go
Two cycles for each pointer iteration
Cycle 1
  Read weightold from weight BRAM
  Read gradient from weight gradient BRAM
Cycle 2
  weightnew = weightold and gradient * learning_rate (0.125 in demo, right shift of 3)
  Write weightnew to weight BRAM
  Increment pointer

## Slide 6: Simple Functional Test of the Training Cycle
Current input data is still random, but let’s assume it is a ‘0’. Since the loss function is not implemented, we can set the loss gradients to be negative for 0 (if neuron 0’s output increases, loss decreases), and positive for the others
  This could be actually be used for the training process down the road since it isn’t so far off from what loss functions are doing
  Otherwise, I can implement loss function using sigmoid: tanh(x)=2σ(2⋅x)−1
    Tanh is supported with a CORDIC core
    Might just be better to set positive gradients for wrong labels and negative for correct for sake of time
In this test, the update only happens in fc2, extension to fc1 and fc0 should be quick. fc2_gradients[0] = -1, all others are 1

## Slide 7: Simple Functional Test of the Training Cycle
Initial Output (Hex simulated and Python script verified)
Out is totally “wrong”, neuron 0 has the 2nd most negative output
  Only converted a few hex numbers to decimal because they have been verified before
-0.26294
-0.09814
0.10620

## Slide 8: Epoch 1

## Slide 9: Epoch 2

## Slide 10: Epoch 3 (0 is now the largest value)

## Slide 11: Epoch 5 (Skipping epochs now) Neuron 0 is now positive

## Slide 12: Epoch 10

## Slide 13: Eventually… (1.65 ms according to sim) Inadvertently, also tested my saturation check

## Slide 14: Going forward
Will start writing report
Now that training is working, want to define an actual loss function that can be used with labels for the MNIST images. I estimate that I will be able to put about 200 images on the FPGA
Ideally, the loss function or signed gradients, although sub-optimal for training, will still be able to realize decent training results, this could allow for a demo

## Slide 15: Exam Date
Thesis hand-in is on Friday, June 28, I fly to the US on Wednesday, July 10.
We have tentatively scheduled the exam for July 8, 2019.