## Slide 1: Thesis Update #1
February 11, 2019
James Erik Groving Meade

## Slide 2: Inference vs. Training (Forward pass or both forward and backward)
Many models implement only the classification on these lower power/computational power accelerators
  This means using a pre-trained networks parameters and simply computing the forward pass of the network
The training component is a bit trickier because there are a lot of intermediate computations and results to be stored and forwarded

## Slide 3: FPGA’s strength: spatial models
FPGA-based models are excellent for implementing a spatial architecture
On the other hand, CPUs and GPUs using temporal models (SIMD) and efficient matrix multiplication via optimized easily via software libraries

## Slide 4: Representing a Deep Neural Network (DNN) in the Accelerator Space
To characterize workload, two main parameters are used, since they take the most time:
  Multiply & Accumulates (MACs)
  Number of weights
Some of the famous DNN’s inference statistics:
  LeNet-5: 431k weights 2.3 million MACs per image
  AlexNet: 61 million weights 724 million MACs per image
  ResNet: 25.5 million weights 3.9 billion MACs per image

## Slide 5: Goals of the Accelerator
Minimize energy usage and maximize speedup
Memory access is a huge bottleneck for FPGA based DNNs
We want to reduce the energy cost by minimizing the distance the memory has to travel, we can do this by employing a hierarchical dataflow
Maximize data reuse (especially relevant for the convolutional layers). Fetching data from a neighboring processing unit is much cheaper than going to DRAM
  Using optimal data reuse in AlexNet can reduce the amount of DRAM reads for inference by roughly ~500x
Balance between DRAM to fetch vs. BRAM and computational resources on the chip

## Slide 6: Minimizing memory reads and maximizing data reuse
The EyeRiss DNN chip from MIT uses a row stationary method to optimize data reuse and minimize amount of BRAM needed per processing element

## Slide 7: Generic vs. Module-Generated Architecture
Some implementations (i.e: EyeRiss, Tabla, Deep-learning processor from Bang 2017) implement a generic processing element (PE) model where the PE performs simple MACs assigned by a central task scheduler
Some other models like F-CNN define modules for specific layers and then have the code generated for the model and placed on the FPGA
Some models define the PE’s to be more than MAC focused, but as collections of modules similar to F-CNN, however, are generic. This is seen in an implementation such as the nn-X chip

## Slide 8: Precision Required
nn-X paper cited a source which claimed Q8.8 is roughly equally accurate to 32 bit floating point
EyeRiss implemented dynamic fixed precision, with a 8-bit dynamic fixed precision weight and 12-bit dynamic activation with only 0.3% accuracy loss
Relevant to minimize amount of memory accesses needed to fetch weight and partial computations
Obviously, in the MACs, partial results will have higher resolution but the end result will be stored in
Side note: recent popular topic is binarized neural networks, where the weights are either 1 or -1, two implementation, BinaryConnect and Binarized Neural Network achieve 19.2% and 29.8% accuracy loss on AlexNet, respectively

## Slide 9: Relevant Metrics
Accuracy
Training time
Energy efficiency
Utilization of resources on FPGA and precision
Number of weights in network
Number of MACs in network

## Slide 10: What models have been done:
The following slides will briefly discuss the architecture of some recently proposed and implemented accelerators:
  EyeRiss Massachusetts Institute of Technology
  Tabla Georgia Tech
  F-CNN Tsinghua University
  nn-X Purdue University
  Unnamed University of Michigan

## Slide 11: Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks
Uses a 12x14 PE array, each PE has MAC and control signals. Design is fixed but can handle any input.

## Slide 12: Questions (and potential answers)
Application: Inference, or both inference and training?
  I would like to try both inference and training
Precision: Floating point, dynamic fixed point, static fixed point?
  Static fixed point for now
Architecture: MAC PE’s, Modular PE’s, Modular-generated?
  Up for discussion. Perhaps a modular PE or modular generated would be easier.
Network to train: LeNet? CIFAR? ImageNet?
  LeNet is quite easy to achieve high accuracy, might not give a good reflection of the effect of reduced precision from FP. ImageNet is a massive scale set. CIFAR is a medium size dataset and the images are relatively non-massive. Therefore, I suggest CIFAR as the dataset to train a network on
Comparison: How to build CPU- and GPU-based models?
  TensorFlow
Need: DRAM to store training data. SoC, ideally with a nice chunk of memory to store weights and partial results to minimize DRAM accesses