## Slide 1: Thesis Update #2
February 18, 2019
James Erik Groving Meade

## Slide 2: Benchmark Model Update
Have implemented CPU/GPU benchmark models on CIFAR10 using Tensorflow. CPU/GPU toggle is done by changing one line of code
I want to change to PyTorch though as the code would be a slightly more readable, portable, and less abstract in what’s going on under the hood
This will not take much longer. Not planning on benchmarking so soon, perhaps GPU can run overnight and CPU over the weekend. Not in a rush at the moment

## Slide 3: Research Aim and Direction
The next few slides will just talk about some relevant papers, the things I’ve learned from them, and how I want to use the findings from these papers to move forward

## Slide 4: Training Deep Neural Networks With Low Precision Multiplications (2015) Courbariaux, David, et Bengio
Paper tests training of networks using artificially lower (by software) precision multipliers for various floating points, fixed points, and dynamic fixed point
“Multipliers are the most space and power-hungry arithmetic operators of the digital implementation of deep neural networks”
Dynamic fixed point algorithm: shift decimal right if overflow rate for a layer > 0.01%, otherwise shift left
Half precision floating point did not affect accuracy that much

## Slide 5: Conclusions from Training Deep Neural Networks With Low Precision Multiplications
“Very low precision multipliers are sufficient for training deep neural networks”
“Dynamic fixed point seems well suited for training DNNS”
Higher precision for updates weights is important
“Our work can be exploited to:
  Optimize memory usage on general-purpose hardware
  Design very power-efficient hardware dedicated to deep learning”
This paper was purely a software implementation of various multiplier precisions, no hardware prototypes were developed

## Slide 6: Training Deep Neural Networks with 8-bit Floating Point Numbers (2018) Wang et Al.
IBM research department developed a 8-bot floating point
  2-4x speedup without compromise in accuracy via two techniques, chunk-based accumulation and floating point stochastic rounding
“These promising results lay the foundation for new hardware platforms that provide significantly improved DNN training performance without accuracy loss”

## Slide 7: Summary:
Specialized accelerators in the domain of DNNs that are primarily focused on performing inference are fairly well-researched (see: TPU, Eyeriss, nn-X)
Previous work on a specialized accelerator for training a DNN (see: F-CNN) used 32-bit floating point without considering reduced precision for better energy-efficiency and speedup
Various types of reduced precision/bitwidths have been proposed and analyzed in several papers, but the application specific training hardware that uses these methods has not been designed/researched much at all
Results from Courbariaux indicate tat even pure fixed point does not hurt accuracy THAT much, good startinhg point

## Slide 8: Next Steps
Port the Tensorflow based benchmarks to PyTorch
Work on a SOFTWARE-first solution that emulates a hardware chip with all relevant restrictions of performing the training. This will make debugging algorithmic and design flaws much easier, and will make the hardware implementation mainly focus on integrating hardware and overcoming hardware issues (like timing, memory, interfacing) and not on design/algorithm issues
  Simulate DRAM interface
  Simulate memory restrictions on chip for weights and activations
  Simulate on-chip processor FPGA MMIO
  Implement the modular but parameterizable network structure similar to F-CNN
  Allow for precision to be specified
ONCE all the algorithm and design of a software based hardware emulator solution, thoughts about translating it to hardware can be started (admittedly, this is a good few steps away!)