## Slide 1: Thesis Update #12
June 13, 2019
James Erik Groving Meade

## Slide 2: Demo!
Inference-only
2. Training with small dataset and frequent stat updates shown
3. Training speed with total disregard for results, only used to show performance with regard to how fast training occurs

## Slide 3: Updates
Implemented a softmax layer to compute a proper loss
Gradient checking in python script verifies that the gradients were indeed correct
Precision issues
Created memory map through DDR SDRAM between ARM and FPGA
Wrote C programs to perform various functions on the FPGA
Created custom BOOT.bin image with the bitstream and U-Boot that invokes a PetaLinux image. Put the MNIST dataset and a few C programs on the SD card.

## Slide 4: Softmax Layer
Why?
  Needed to calculate using an actual loss function for gradients, otherwise unable to learn properly
Softmax is one of the best loss functions for training neural networks
Mathematically:

## Slide 5: Softmax Layer Structure
Convert to float
Perform ex
Convert back to fixed
Sum all ex
Divider core
Derivative is quite simple for softmax. It is just the output of the softmax for non-label neurons, and output minus 1 for the label neuron
Pipelined for the 10 output neurons, takes about 50 cycles for the 10

## Slide 6: Also… don’t set the divider IP core to 1 cycle

## Slide 7: Verification of Softmax
… I found out that SystemVerilog/Verilog can display floating point, so it’s quite quick to visually verify now. Output from the softmax layer, and previous neuron gradients vs. Python script
Python
FPGA
Python

## Slide 8: So, softmax seems to be verified. Training still off, why? Could the Python script be wrong?
Wrote gradient check testing in the python script to verify that the script was indeed correct. So the calculated gradients are correct.

## Slide 9: What’s going on, if the gradients calculated are correct, why isn’t it training to perfection!
This reminded me of a paper I read back in February
The below graph was a part of it

## Slide 10: My theory
Observe the gradients from the simulation
Gradients in general want to push up the correct neuron by a lot, and at the same time lower the other gradients a bit
The gradients are Q3.13, activations are Q8.8
  When updated, these are multiplied by 0.001, or shifted to the right by 10. Only 3 fractional bits remaining, so gradients effectively truncated at 0.125 steps.
  Result is that many of the gradients that “push” final layer neuron output down get effectively truncated to zero, and as a result, the pushing up is much stronger than the pushing down
Recall the the train_small example, learning happens, as the accuracy does occur, but if neuron output is only pushed up, then eventually they will all saturate

## Slide 11: Solution: More Precision Needed if Training is to be Supported
Will try 24-bit and 32-bit solutions to see if the precision is good enough for training.
Most important part is that the negative gradients multiplied by around 0.001 will not disappear
Probably prioritize writing the design and testing section of report for now though, since this is more of a result section asepct.

## Slide 12: FPGA Clock Frequency
FPGA being at 50 MHz, should I try to get it back to 100 MHz?
  No, DDR transmission is the bottle neck, as observed by the active cycle percentage
Also, active cycle percentage is ~2x for training compared to inference.
This is because training is ~2x more cycles, so roughly ~2x more time to load the next image
Inference
Training
50 MHz timing met

## Slide 13: Timing/Results
Faster than CPU by a lot, on both inference and training
GPU
  Faster for batch size of 1, but I discovered the PyTorch framework GPU training uses a coarser-level of parallelism. It doesn’t parallelize the computation of a single input, but instead parallelizes the input samples in a batch. I.E input 1 to a core, input 2 to another core, and so on
  Therefore it’s unfair to compare against GPU batch size of 1, since it doesn’t parallelize at that level
  Example timing for batch size of 5 and 200 shown below (though this means it performs (batch size - 1 fewer updates than my batch size = 1 model)

## Slide 14: Timing/Results
For training on 60,000 training images, then inference on 10,000 test images
My Software Model, CPU
PyTorch: Batch size of 5, GPU
FPGA Accelerator
PyTorch: Batch size of 200, GPU
PyTorch: Batch size of 1, CPU

## Slide 15: Timing in a neat table
Model | Time for 1 Training Epoch
Software Model, Batch Size = 1 | 275.95 seconds
PyTorch CPU, Batch Size = 1 | 122.65 seconds
PyTorch GPU, Batch Size = 5 | 74.93 seconds
PyTorch GPU, Batch Size = 200 | 7.14 seconds
Hardware Model, Batch Size = 1 | 4.61 seconds

## Slide 16: Memory Map between PS and FPGA
Created a memory map so that data can be sent over DDR
CPU side: handle to /dev/mem with a pointer at the offset specified by the Zynq PS system in Vivado
FPGA side: AXI slave interfacing with the AXI Master from Zynq PS

## Slide 17: FPGA Side
Based on a modified Vivado provided Axi core
FPGA to PS
PS to FPGA

## Slide 18: FPGA Side

## Slide 19: FPGA Side
Defining the Virtual Address Space
Generated the block diagram from previous slide. Then created and instantiated the wrapper in my neural_net_top.sv file and forward inputs/outputs
In neural_net_top.sv

## Slide 20: ARM Core

## Slide 21: Training Programs
Easier to show than put on slide

## Slide 22: Customized Boot Images
Exported hardware to Xilinx SDK, allows me to create a boot image with first-stage boot loader, bitstream, and U-Boot
Then put on a root file system and PetaLinux image
Root file system could be modified in a linux distribution, modified init.d/rcS to assign the Zedboard an IP of 192.168.1.10 for SCP/SSH and to mount the SD card

## Slide 23: Power measurements?
Will I be able to do this now that I have something benchmarkable running?

## Slide 24: Report Writing
Have about 15 pages written so far, now that I’ve finished most of what I want to do, can put most time into that. Would ideally like to increase precision on FPGA, but 2 concerns, 1 being time and 1 being that the resource usage might be too high if I increase precision:

## Slide 25: Exam Date
Seems we have confirmed for July 8! Very happy to hear, will wait for confirmation of the time slot.