## Slide 1: Thesis Update #5
April 1, 2019
James Erik Groving Meade

## Slide 2: Agenda
Updates on the software model
Updates to the model test network architecture
Scope of FPGA implementation
Some ZedBoard stuff

## Slide 3: Software model
Added momentum, results in faster convergence, though the implication is that an extra value will be needed per weight
Modified the loss function to be better for image classification
Image to the right is training the network on 50 random input samples in a 3-layer network
Expected to test on CIFAR 10 this week

## Slide 4: New Network Architecture
Fits in BRAM, and will be able to fit gradients and momentum information
Trains to ~60.3% accuracy on CIFAR10, once started on FPGA, also plan to try modifying for MNIST (handwritten digits), input layer changes from 32x32 to 28x28 in this case, but can make the 28x28 a 32x32 with padding or can change outer layer
9 Layers, details in coming slides

## Slide 5: Layers
1 – Input Layer: 3 (R, G, and B) channels, 32x32 each
2 – Convolutional, 3x3x3 filter, stride of 2, 6 output feature maps of size 16x16
  41,472 weights
3 – 2x2 Max Pooling  Output is 6 channels of size 8x8
4 – Convolution  3x3x6 filter, stride of 1, 8 output feature maps of size 8x8
  27,648 weights
5 – 2x2 Max Pooling  Output is 8 channels of size 4x4

## Slide 6: Layer Continued
6 – Convolutional  3x3x8 filter, stride of 1, 10 output features maps of size 4x4
  11,520 weights
7 – Fully Connected  10 * 4 * 4 input, 32 neuron output
  5,120 weights
8 – Fully Connected 32 in, 10 out
  320 weights
9 – Softmax output layer, converts logits to probabilities

## Slide 7: Summary of weight storage
There are 86,080 weights in this network
For each weight, also store a gradient and momentum value, chip will store 86,080 * 3 = 258,240 values
Each value will be stored in 16 bits, or 2 bytes
516,540 bytes total
There is 645,120 bytes of BRAM available, can fit all weights and the rest of the BRAM will be used for storing activations

## Slide 8: A Note on Activations
Amount of data required for activation data for an image:
  Conv1 – 1536 activations
  Conv2 – 512 activations
  Conv3 – 160 activations
  FC1 – 32 activations
  FC2 – 10 activations
2,250 activations total  4,500 bytes per image
Hypothetically if could use all of the remaining BRAM (~129,000 bytes), could store 28 images worth of activations
Quite common batch size is 64. This would require to saves and loads of activations to DRAM. (28 + 28 + 8)

## Slide 9: Scope of Implementation
One of the requirements of a dynamically generated HDL training network would be that the BRAMs would have to be dynamically allocated
This is rather difficult, will start with a non-generated HDL implementation using modular layer modules that can be tuned easily and manually instantiated BRAM

## Slide 10: Notes on the ZedBoard
Have booted up the ZedBoard and able to connect via PuTTY over terminal, ran simple LED read/write programs on the provided boot setup
Considering throwing PetaLinux on as the OS so that the boot image isn’t reloaded from a g-zipped file each time and ease of cross-compiling
Ideal would be to connect it to network and SSH in, also easier to transfer files this way, perhaps need to do using a router ?
There is a DRAM Xilinx module that can handle DDR3